Basic Electrical

Tutorial 1 (Basic Requirement)

- Find the total resistance between point A and B

- The resistance of two conductors is 25 Ω, when connected in series, and 6 Ω, when connected in parallel. Determine the individual resistance of the two conductors. (Ans. 15Ω,10Ω)

- A resistor of 8 Ω is connected in series with a combination of 12 Ω and 24 Ω in parallel. The whole circuit is connected across 100 V supply. Find :

  - The current taken from the supply; (6.25A)

  - The voltage across 8 Ω resistor and (50V)

  - Current flowing in 12 Ω and 24 Ω resistor.(4.17A, 2.08A)

- In the circuit shown in fig.4, the total power dissipated is 488 W. determine the current flowing in each resistor and voltage between A and B.(2A,0.5A,4A and 75V)

- Determine the value of R, if the power dissipated in 10 Ω resistor is 40 W for the circuit shown in fig.5.(34.29Ω)

- The current in 6 Ω resistor of circuit as shown in fig.6 is 2 A. find the current in all other resistors and voltage V across the circuit.(46V)

- Find the total resistance between point A and B, using star/delta transformation.fig.7

- Find the total current supplied by the battery, using star/delta transformation.fig.8

******

# Text boxes

10Ω

40Ω

20Ω

A

B

18Ω

3Ω

6Ω

3Ω

Fig.1 a) 5.714Ω

8Ω

A

B

Fig.1 b) 10.6Ω

Fig.4

B

A

10Ω

2.5Ω

20Ω

5Ω

Fig.5

V

50V

10Ω

R

40Ω

80Ω

Fig.5

4Ω

6Ω

6Ω

8Ω

8Ω

A

B

Fig.7 (468.5Ω)

200Ω

300Ω

400Ω

800Ω

600Ω

10Ω

10Ω

20Ω

50Ω

50Ω

Fig.8 (3.33A)

13.3Ω

100V